## Slide 1
Parallelizing CNNs
CPU → CUDA → Multi-GPU
A measured MNIST case study: the same convolution on CPU, CUDA, cuDNN and two GPUs.
CPU
few powerful cores
CUDA GPU
many parallel threads
2× GPU
batch split + sync
PRITHIV • CNN + CPU
SATYA • CUDA + KERNELS
ROYDON • RESULTS
50 epochs · 10% MNIST · Kaggle T4 ×2
Notes: CNN CUDA Case Study. Prithiv explains the CNN and CPU; Satya explains CUDA and DataParallel; Roydon presents measured results and runs the saved checkpoint demo. The cover is followed by eleven content slides.

## Slide 2
How a CNN works — in one slide
Our digit classifier: 28×28 image → convolution → ReLU/pool → 676 features → ten class scores.
PRITHIV · PERSON 1
1 • INPUT IMAGE
28×28
2 • CONVOLUTION
4 filters × 3×3
26×26 outputs
3 • FEATURE MAPS
4 feature maps
local patterns
4 • ReLU + POOL
ReLU
Pool
5 • CLASSIFY
0–4
5–9
Batch 64 performs 1.56 million multiply–accumulates in this convolution.
Each output is a separate weighted sum: a natural parallel work item.
Notes: Prithiv Follow the picture from input to predicted digit. A filter performs a weighted sum over a small image patch. The same learned weights scan every location. Multiple filters learn different responses. ReLU replaces negative responses with zero; max pooling retains the largest response in each 2x2 region. The actual shapes are 1x28x28 -> 4x26x26 -> 4x13x13 -> 676 -> 10 logits. The CNN has 6,810 parameters. Cross entropy compares the scores with the true label; backpropagation and SGD adjust the weights. The illustration is conceptual, not a captured activation from a trained model. Reference: https://docs.pytorch.org/docs/2.9/generated/torch.nn.Conv2d.html Measured implementation: https://github.com/saltypal/CNN-CUDA-Case-Study/tree/370e8a418f76c32129057a95eb7993f19095cd3f/src/hpc_cnn

## Slide 3
Where parallelism helps in a CNN
Sequential logic does the same independent work one piece at a time; parallel execution does many pieces together.
PRITHIV · PERSON 1
SEQUENTIAL
One worker repeatedly computes output cells
1
2
3
4
5
6
7
8
time →
Nested loops cover batch, filters and pixels
One worker computes each complete weighted sum
Different output cells are independent
PARALLEL
Many workers compute independent cells together
T1
T2
T3
T4
T5
T6
T7
T8
same time window
CONV / GEMM
ACTIVATION
POOLING
BATCHES
Best target: many independent output sums.
Limits: tiny jobs, launch overhead and synchronization.
Notes: Prithiv The arithmetic stays the same. Each output is bias plus the sum of input*weight products in its receptive field. Different outputs do not depend on each other, so they can have separate workers and separate writers. The image has 2,704 outputs; batch 64 has 173,056. This makes convolution a useful source of data parallelism. Parallelism is most useful when there is enough work to offset scheduling and communication. It also appears in other CNN operations. Weight gradients require combining contributions because every image uses the same filter weights; the optimizer waits for those gradients. Parallel layers do not remove the forward -> loss -> backward dependency. The toy diagram shows four outputs. Worker icons are conceptual, not physical-core counts. Measured implementation: https://github.com/saltypal/CNN-CUDA-Case-Study/tree/370e8a418f76c32129057a95eb7993f19095cd3f/src/hpc_cnn

## Slide 4
How a CPU executes a CNN
OpenMP assigns independent outputs to CPU threads. SIMD processes multiple values per instruction.
PRITHIV · PERSON 1
CPU VIEW
CPU
T0
T1
T2
T3
OpenMP splits output cells
among four CPU threads.
One writer per output.
Input and weights are read-only.
ADVANTAGES
Low overhead; no GPU transfer
OpenMP threads share the input data
Good latency for small requests
LIMITS FOR CNNs
Fewer concurrent workers than a GPU
Threads share cache/memory bandwidth
Coordination can outweigh tiny jobs
CPU: low request latency
GPU: high batch throughput
Notes: Prithiv The native C++ code has an outer output loop and inner channel/filter loops. OpenMP parallel-for with static scheduling distributes outer-loop iterations among four logical CPU workers. Each iteration has a local accumulator and stores a different output, so the forward pass needs no atomic addition. Caches reuse nearby image data. OpenMP adds threads; SIMD vectorization is a separate mechanism, and its exact use was not inspected. Several CPU workers still share memory resources. These are practical limits to ideal scaling, not proof of a specific bottleneck percentage. The illustration shows read-only input and weights feeding separate output owners. The native CPU microbenchmark is distinct from PyTorch CPU training. Reference: https://www.openmp.org/spec-html/5.2/openmpse66.html Measured implementation: https://github.com/saltypal/CNN-CUDA-Case-Study/tree/370e8a418f76c32129057a95eb7993f19095cd3f/src/hpc_cnn

## Slide 5
GPGPU: using the GPU for general computation
A GPU is not only for graphics. GPGPU uses its many simple compute lanes for data-parallel workloads such as CNNs.
SATYA · PERSON 2
CPU
Few complex cores
Optimized for latency, branching and control
GPGPU
Many lightweight compute lanes
Same operation applied to lots of data at once
Why CNNs fit
Output pixels
PARALLEL
Filters / channels
PARALLEL
Images in batch
PARALLEL
Matrix multiplies
PARALLEL
Batches expose many independent output sums.
Useful work must outweigh launch and data-movement costs.
Notes: Satya GPGPU means general-purpose computing on a graphics processing unit. A GPU has many arithmetic resources designed for throughput. A CPU has fewer, more complex general-purpose execution resources and often lower overhead for a small request. Neither wins every workload. CNN convolution exposes many similar independent sums. Bigger batches and feature maps provide more work for GPU scheduling. Moving tensors to a separate device and submitting kernels still costs time. These benchmarks distinguish resident data from transfer costs. The chip illustration is conceptual and does not claim an exact hardware core count. Reference: https://docs.nvidia.com/cuda/archive/12.8.0/cuda-c-programming-guide/index.html Measured implementation: https://github.com/saltypal/CNN-CUDA-Case-Study/tree/370e8a418f76c32129057a95eb7993f19095cd3f/src/hpc_cnn

## Slide 6
How CUDA turns a GPU into a parallel program
CUDA lets the CPU launch GPU kernels as a hierarchy of grids, blocks and threads.
SATYA · PERSON 2
HOST / CPU
1
Upload tensors once
2
Choose grid & block
3
Launch kernel
4
Wait for completion
DEVICE / GPU
Grid
Block 0
Block 1
Block 2
Block 3
One output per thread; 256 threads per block.
Memory
Registers
fastest
Shared
per block
Global
large
CUDA exposes concurrent work; shared-memory reuse is an optimization to test.
Notes: Satya CUDA is NVIDIA's programming platform for this GPU work. The CPU launches a grid of blocks; the GPU schedules the blocks on streaming multiprocessors. Our direct convolution uses one logical thread per output, with 256 threads per block. Logical threads are not equivalent to physical CUDA cores, and all threads need not execute simultaneously. Threads accumulate products using the same kernel code and different indices. Shared-memory tiling can reduce repeated source-level reads, but cooperative loading and barriers add cost. In the saved measurements it was slower than direct CUDA. The host launch is asynchronous. A completed-call wall measurement synchronizes before stopping the timer; enqueue time alone would not measure convolution completion. Reference: https://docs.nvidia.com/cuda/archive/12.8.0/cuda-c-programming-guide/index.html Measured implementation: https://github.com/saltypal/CNN-CUDA-Case-Study/tree/370e8a418f76c32129057a95eb7993f19095cd3f/src/hpc_cnn

## Slide 7
CUDA kernels in the CNN program
A kernel is the GPU function executed by many threads. We map CNN operations to kernels, then choose how much control to keep.
SATYA · PERSON 2
INPUT
CONV
ReLU
POOL
FC
OUTPUT
Same model, data, loss and SGD. Custom kernels replace convolution forward and backward.
CONV KERNEL MAPPING
Forward convolution
Thread → one output; 256 threads/block
Each output sums nine products plus bias
Tiled variant → 16×16 outputs reuse 18×18 input
Backward: block reductions sum the weight gradients.
PROGRAM DESIGN
PyTorch
Layers, loss, autograd, SGD
shared wrapper
cuDNN
Direct library convolution
fixed algorithms
CUDA
Custom CUDA convolution
thread control
All paths use the same CNN. PyTorch GPU also invokes cuDNN.
Notes: Satya A kernel is a device function executed by many CUDA threads. Our index is blockIdx.x*blockDim.x+threadIdx.x. Each valid thread decodes its sample, filter, row and column, then writes one complete output. The first layer has one input channel and four 3x3 filters, so each output uses nine multiply-accumulates plus bias. All programs share ReLU, pooling, linear classifier, cross entropy and SGD. The controlled comparison changes convolution and, for two-GPU runs, the DataParallel wrapper. Custom backward kernels compute parameter gradients using partial sums and a block reduction. Input gradients are supported and validated, but raw MNIST input does not require them during training. Direct cuDNN uses fixed convolution algorithms through its C API. PyTorch GPU also used cuDNN in the observed trace. No Tensor Core usage was verified. The three paths represent program/API and algorithm choices, not three different GPU hardware types. Measured implementation: https://github.com/saltypal/CNN-CUDA-Case-Study/tree/370e8a418f76c32129057a95eb7993f19095cd3f/src/hpc_cnn

## Slide 8
How DataParallel works across two GPUs
Split batch 64 across two replicas; gather logits, backpropagate and sum parameter gradients on GPU 0.
SATYA · PERSON 2
FORWARD + BACKWARD FLOW
BATCH
64 images
scatter
GPU 0
model replica
32 images
GPU 1
model replica
32 images
GPU 0
Gather logits
Sum gradients
optimizer
updates model
What we had to handle
Correct device + current stream
Per-device cuDNN state
Save unwrapped checkpoints
Benefit
more batch work at the same time
Cost
scatter + gather + synchronization overhead
Extra GPUs help only when saved computation exceeds replication and communication costs.
Notes: Satya PyTorch DataParallel replicates the module, scatters the batch, runs each replica and gathers outputs on the primary device. We compute one mean cross-entropy loss over the gathered batch. Backward sums both replicas' parameter gradients into the original module; one SGD optimizer updates it. The global batch remains 64 instead of increasing to 128, which preserves the experiment workload and optimizer behavior. Our native wrappers use the tensor's device and current stream; direct cuDNN state is cached by device. A batch of one creates only one useful input chunk, so single-image latency does not benefit from a second replica. Reference: https://docs.pytorch.org/docs/main/generated/torch.nn.DataParallel.html Measured implementation: https://github.com/saltypal/CNN-CUDA-Case-Study/tree/370e8a418f76c32129057a95eb7993f19095cd3f/src/hpc_cnn

## Slide 9
Results 1/4 — Measured CNN performance
50 epochs · 4,800 train / 1,200 validation / 1,000 test · identical model, weights and batch 64.
ROYDON · PERSON 3
FASTEST TRAINING
5.42 s
PyTorch · one T4
1.88× faster than CPU
Latency vs throughput
CPU: 83.45 µs per digit.
CUDA: 178,698 batch img/s.
The best path depends on how much work is submitted.
Conv/Infer: one-digit µs, resident input. Batch/s: batch-64 inference.
Training excludes warmup/validation/I/O; batch-one DP uses one replica.
Implementation | Train (s) | Conv (µs) | Infer (µs) | Batch/s
PyTorch CPU | 10.17 | 23.80 | 83.45 | 59,454
CUDA · 1 GPU | 6.06 | 62.41 | 351.39 | 178,698
CUDA · 2 GPUs (DP) | 15.99 | 548.40 | 913.92 | 29,441
cuDNN · 1 GPU | 6.34 | 141.80 | 444.74 | 142,844
cuDNN · 2 GPUs (DP) | 17.32 | 633.95 | 959.52 | 27,024
PyTorch · 1 GPU | 5.42 | 41.68 | 379.61 | 169,365
PyTorch · 2 GPUs (DP) | 18.39 | 524.17 | 867.08 | 20,903
Notes: Roydon All seven models completed 50 epochs on Kaggle T4 x2. The balanced 10% MNIST subset contains 4,800 training, 1,200 validation and 1,000 test images. Seed 42, batch 64, identical initial weights, FP32, SGD learning rate 0.05 and momentum 0.9 are shared. TF32 is disabled. All 170 correctness checks passed. Training time sums synchronized training epochs and excludes warmup, validation, initial transfer and checkpoint I/O. All final epoch-50 checkpoints predict 956 of 1,000 test examples correctly. PyTorch with one GPU is fastest here at 5.42 s; CPU takes 10.17 s. Two-GPU DataParallel is slower than its matching one-GPU path. This is one seed and one runtime. It is a case study rather than a universal hardware ranking. Measured implementation: https://github.com/saltypal/CNN-CUDA-Case-Study/tree/370e8a418f76c32129057a95eb7993f19095cd3f/src/hpc_cnn
Training time is the sum of synchronized epochs. Batch/s measures full-CNN inference at batch 64, not training throughput. Source commit: 370e8a418f76c32129057a95eb7993f19095cd3f.

## Slide 10
Results 2/4 — Two-GPU scaling and overhead
Matching engines, same global batch 64. Extra GPUs increased training time for this small CNN.
ROYDON · PERSON 3
TRAINING TIME
CUDA
cuDNN
PyTorch
Training time (s)
Same batch 64; lower is better
1 GPU
2 GPU DP
Two GPUs took 2.64–3.39× longer
EFFICIENCY & COST
Two-GPU efficiency
14.7–19.0%
GPU-time cost ratio
5.27–6.78×
WHY TWO GPUs LOST
DP adds replication, scatter/gather and gradient reduction
This CNN is too small to offset those costs
GPU-time is a proxy; energy/currency were not measured
6.06
15.99
6.34
17.32
5.42
18.39
0
5
10
15
20
Notes: Roydon The operation column measures one convolution on a single digit: input 1x1x28x28, four 3x3 filters, bias and output allocation. Inference measures the entire CNN forward pass. Both are warmed medians of completed-call wall latency with input resident on the device. Batch infer/s uses a batch of 64, unlike the one-image columns. PyTorch CPU has the lowest single-image inference latency. Custom CUDA has the highest batch-64 inference throughput in this runtime. These two workload scopes need not have the same winner. DataParallel single-image calls use one replica and still pay wrapper costs. The handwritten C++ convolution, benchmarked separately, takes 124.06 us with one worker and 66.32 us with OpenMP. At batch 64, it improves from 6608.54 to 2244.91 us: 2.94x on four logical workers. Do not confuse that native baseline with optimized PyTorch CPU convolution. The tiled custom CUDA variant was also benchmarked, but did not improve the direct kernel in any saved case. Measured implementation: https://github.com/saltypal/CNN-CUDA-Case-Study/tree/370e8a418f76c32129057a95eb7993f19095cd3f/src/hpc_cnn
Bars are actual 50-epoch training times. Speedup T1/T2: CUDA 0.379, cuDNN 0.366, PyTorch 0.295. Efficiencies: 18.96%,18.30%,14.74%. GPU-time ratios:5.27,5.47,6.78. No batch-size sweep or utilization telemetry was measured.

## Slide 11
Results 3/4 — Accuracy and numerical checks
All seven final models classified 956 of 1,000 test digits correctly. All 170 correctness checks passed.
ROYDON · PERSON 3
CPU accuracy
95.6%
1-GPU accuracy
95.6%
2-GPU accuracy
95.6%
Max forward |Δ|
3.58e-07
CHECK
Same input, same weights, same FP32 precision
CPU output
≈
GPU output
≈
2-GPU output
170 checks passed: forward and input/weight/bias gradients, including non-square inputs and partial tiles.
INFERENCE
Every final model: 956/1,000 correct
Same data, initialization and precision
Forward and all gradients passed
50 epochs completed in every path
Same accuracy; lower wall time on one GPU.
Notes: Roydon The comparison holds the global batch at 64 and uses the matching one-GPU engine as the baseline. Training speedup is T1/T2. Efficiency is speedup divided by two. A speedup below one means the two-GPU run took longer. GPU-time cost is 2*T2/T1, a time-based resource proxy rather than monetary billing, energy or Kaggle quota use. The small convolution does not supply enough per-replica work to compensate for replication, host dispatch, scattering, gathering and gradient reduction. These costs are real, but no profiling attribution was collected to prove what exact percentage each contributes. The report saves host enqueue, instrumented device intervals, transfers and an identity DataParallel diagnostic; the latter is not an exact subtraction of CNN communication cost. Energy was not measured. No monetary rate was provided. Logical tensor bytes and FLOP counts, measured memory and timing are separate quantities. For this model, one GPU is the better training choice. Measured implementation: https://github.com/saltypal/CNN-CUDA-Case-Study/tree/370e8a418f76c32129057a95eb7993f19095cd3f/src/hpc_cnn
The displayed max error is the maximum absolute error among all forward validation checks against the framework reference; it is not a gradient-error maximum or a training accuracy difference.

## Slide 12
Results 4/4 — Inferences and live demo
Choose hardware by workload: CPU for small requests, one GPU for batches, more GPUs only when scaling pays.
ROYDON · PERSON 3
1
Convolution exposes parallel work
Different outputs execute independently; shared weight gradients require reductions.
2
CPU wins tiny-request latency
83.45 µs per digit in this run. Framework and launch overhead matter.
3
One GPU wins this training run
PyTorch/T4: 5.42 s for 50 epochs vs CPU 10.17 s. All models: 95.6% test accuracy.
4
Two GPUs need enough work
DataParallel: 15.99–18.39 s. Communication outweighed the saved compute time.
Final design takeaway
CPU for tiny requests → one GPU for batched work → two GPUs only when synchronization pays.
Demo: seven checkpoints → the same held-out digits → predictions and true labels.
Notes: Roydon Conclude with the workload, not a blanket CPU-versus-GPU claim. The CPU wins single-image latency in this run; one GPU wins training and batched throughput. More GPUs are useful only when additional parallel compute exceeds orchestration and communication costs. Every final model has 95.6% test accuracy. Demo: load the seven final checkpoints and predict the same held-out digits. The script already ran successfully in the completed Kaggle notebook. It does not retrain. Its cold loading time is not the warmed inference benchmark. cd /kaggle/working/cnn-cuda-case-study-source PYTHONPATH=src python -m hpc_cnn.demo --run-root /kaggle/working/cnn-cuda-case-study-results A live run of all paths requires two GPUs. Keep the saved logs and predictions ready as an offline backup. The experiment is one seed and one runtime. Measured implementation: https://github.com/saltypal/CNN-CUDA-Case-Study/tree/370e8a418f76c32129057a95eb7993f19095cd3f/src/hpc_cnn